## Slide 1: Mechanical engineering intro
Links and Guides

## Slide 2: What is mechanical Engineering?
Definition:
  Branch of engineering that focuses on the design, production, analysis, working and improvement of a technical object.
  In other words it looks at how things work!

## Slide 3: To understand how an object works one must consider:
  Guides
  Links
  Motion Transmission
  Motion Transformation
  Speed change

## Slide 4: Links
Linking is the mechanical function performed by any component that connect different parts of an object.

## Slide 5: Links
Four key characteristics of a link
  Direct vs. indirect
  Rigid vs. Flexible
  Removable vs. Non-removable
  Complete vs. Partial

## Slide 6: 1: Direct vs. Indirect
A link is direct when two objects hold together without a linking component
A link is indirect when the parts need something else (a linking component) to hold them together
    Ex: glue, sticky tack, nails, screws …
Glue

## Slide 7: 2: Rigid vs. Flexible
A link is rigid when the linking component or the surfaces of the linked parts are rigid
A link is flexible when the linking component or the surfaces of the linked parts can be deformed.
  Ex: springs, rubber, Sticky tack

## Slide 8: 3: Removable vs. non-removable
A links is removable when the linked parts can be separated without damaging either the surfaces of the linking component.
  Ex:. nail, screw, nut and bolts
A link is non removable when separating the linked parts damages their surface or the linking component
  Ex:. glue

## Slide 9: 4: Complete vs. Partial
A link is complete when it prevents the linked parts from moving independently of one another
  Ex:. nail …
A link is partial when at least one part can move independently of the other part
  Ex:. hinges …

## Slide 10
Linkages
Can the object be taken apart without causing damage to the object?
Non-removable
Is movement possible between the two parts?
Complete
Is the fastener that links the parts together flexible ?
Flexible
Do the parts require something else to hold them together?
Indirect
Direct
Rigid
Partial
Removable
no
yes
no
no
no
yes
yes
yes

## Slide 11: Describe the type of link
direct or indirect,
rigid or flexible,
non-removable or removable,
complete or partial,
Indirect
Rigid
Removable
Partial
The “link” between the hinge and the doorframe:

## Slide 12: Describe the type of link
direct or indirect,
rigid or flexible,
non-removable or removable,
complete or partial,
Direct
Rigid
Removable
Complete
The “link” between the pen and the cap:

## Slide 13: The types of « Links » between Parts
The “link” between the handle and the punch is:
?
direct or indirect,
rigid or flexible,
non-removable or removable,
complete or partial,
.
Direct
Rigid
Non-removable
Complete

## Slide 14: The types of « Links » between Parts
The “link” between the bottom handle and the top handle is:
?
direct or indirect,
rigid or flexible,
non-removable or removable,
complete or partial,
.
Indirect
Rigid
Non-removable
Partial

## Slide 15: The types of « Links » between Parts
The “link” between the bottom handle and the receptacle is:
?
direct or indirect,
rigid or flexible,
non-removable or removable,
complete or partial,
.
Direct
Flexible
Removable
Partial

## Slide 16: Principle Types of Links
6 key types; based on the type of motion by the linked part
1: Fixed link: no movement

## Slide 17
2: Rotating link: rotational movement around 1 axis

## Slide 18
3: Sliding link: translational movement around 1 axis

## Slide 19
4: Sliding/rotating link: rotational + translational movement around 1 axis

## Slide 20
5: Spherical link: multiple rotational motion

## Slide 21
6: Helical link: helical motion

## Slide 22: Guides
A guiding component is a component whose mechanical function is to guide the motion of moving parts
Types of guides
  Translational guide
    Ensures the straight translational motion of a moving part
    Symbol for translational movement

## Slide 23
  Rotational guide
    Ensures the rotational motion of a moving part
    Symbol for rotational movement

## Slide 24
  Helical guide
    Ensures a combination of translational and rotational motion of a moving part
    Symbol for helical movement